## Slide 1
Predictive Modeling of Building Energy Efficiency
Robert Gravatt | DATA 201 | April 30, 2026

## Slide 2
1 & 2. Project Scope & Strategy
Bridging Design & Science
Sustainable architecture requires the ability to predict thermal behavior before construction. We leverage the UCI Energy Efficiency dataset to bridge architectural geometry with energy demand.
Key Target Variable: Heating Load (kWh/m²)
Goal: Determine if architectural parameters like height, surface area, and compactness can reliably forecast energy efficiency requirements.

## Slide 3
3. Dataset: Variable Overview
Feature Group | Specific Variable | Description
Geometric | Relative Compactness | Measure of building shape efficiency.
Envelope | Surface Area / Roof Area | Total structural exposure measurements (m²).
Massing | Overall Height | Binary split: 3.5m vs 7.0m structures.
Environmental | Orientation / Glazing | Building direction and window distribution.
Target | Heating Load | Energy required for heating (kWh/m²).

## Slide 4
Methodology: Data Cleaning
Relabeling: Transformed generic "X1-Y2" indices into descriptive architectural features for interpretability.
CSV Cleanup: Addressed trailing delimiters and ghost columns from spreadsheet exports to ensure matrix alignment.
Validation: Verified 768 complete observations with zero missing values via df.info() check.
Splitting: Identified "Overall Height" as the primary binary predictor for bimodal performance analysis.

## Slide 5
4a. Heating Load Distribution
Bimodal Clusters
The histogram reveals two distinct performance clusters. This suggests a primary design factor creates a "split" in thermal behavior.
•
Efficient Designs: 10–15 kWh/m²
•
High-Demand Designs: 25–35 kWh/m²

## Slide 6
Height: The Primary Driver
Height vs. Compactness
By color-coding the scatter plot by Height, we observe that vertical massing is the primary determinant of demand.
Regardless of compactness, 7.0m buildings consistently require more energy than 3.5m structures.

## Slide 7
Numerical Evidence: Correlation
Feature Importance
The correlation matrix quantifies the physical drivers of energy efficiency:
0.89 correlation: Overall Height
0.62 correlation: Relative Compactness
0.00 correlation: Orientation (Negligible)

## Slide 8
Modeling: Baseline vs. Improved
Baseline
Multiple Linear Regression assuming additive effects. Achieved 91% starting accuracy.
Reasoning
Thermal physics is non-linear. Interactions (e.g., Height x Surface Area) better reflect structural reality.
Improved Model
Polynomial Features (Degree 2) captured non-linear interactions, raising accuracy to 99%.

## Slide 9
4b-e. Performance Benchmark
By introducing interaction terms, we reduced prediction error (RMSE) from 3.02 to 0.80 kWh/m².

## Slide 10
4g. Final Predictive Validation
Testing the model on three unique design scenarios from the test set:
Design Sample | Actual Load | Predicted Load | Model Error
Building Design 1 | 16.47 kWh/m² | 16.56 kWh/m² | 0.09
Building Design 2 | 13.17 kWh/m² | 13.32 kWh/m² | 0.15
Building Design 3 | 32.82 kWh/m² | 32.79 kWh/m² | 0.03